## Slide 1
D. Barnett, K. Rainwater, J. C. Dickens, A. Neuber, J. Mankowski
Center for Pulsed Power and Power Electronics (P3E)
Department of Electrical Engineering
Texas Tech University
Box 43102, Lubbock, TX 79409-3102, USA
2017 Pulsed Power Conference
June 18th – 22th, Brighton, UK
Results of A Compact Reflex Triode With Multi Cavity Adjustment

## Slide 2: Overview
Background and Motivation
  Cathode
  Anode
  Tube Structure
Experimental Setup
  Sealed Tube Reflex-Triode Vircator
  Pulsed Power Source
Experimental Results
  Frequency tunability comparison
Future Work
Notes: Quickly skim through this

## Slide 3: Old Tube Performance
Only a few main frequencies
Low power at a large majority
Limited ability to adjust performance

## Slide 4: Cathode and Anode
Bimodal carbon-fiber (CF) cathode
2 million CF pyrolitically bonded to a POCO graphite substrate
Rogowski-profile
2.5” diameter
Pyrolitic graphite anode
Long life time >100,000 shots
High thermal emissivity
70% transparent
3.5” diameter
SEM imaged eroded CF tip
Electron source  Explosive emission induce plasma

## Slide 5: Cathode Conditioning
Tube Preparation
  Extreme cleaning of internal components
  Plasma cleaning of smaller components
  Bake out at 175℃ for 72 hours while connected to a turbo molecular pump
Procedure
  >1,000 shots minimum
  Shots taken at 10Hz, 20 shot burst
  50 kV charging voltage
  8 mm A-K gap

## Slide 6: Square Waveguide Structure
Waveguide
  4.91”(124.7mm) X 5.58”(141.7mm)
    W X H
  1.58”(40mm) Bottom Plate travel
    a = 4.91”, b = 5.58 “, m = 1, n =0

## Slide 7: Sealed Tube Reflex-Triode Vircator
Diagnostics
Capacitive Voltage Divider
Person Current Monitor
Wide Band Receiving Antenna
Tube characteristics
Background pressure: ≈ 10-9 Torr
  Backed by a 20 L/s ion pump
8” Tube
Internal liner
Movable Backwall (BW)
Movable Bottom Plate(BP)
Adjustable Anode –Cathode Gap (AK gap)
Sealed tube

## Slide 8: Pulsed Power Source
12 stage PFN-based Marx Generator
  Rayleigh PFN
  50 kV charging voltage
  600 kV output @ 50 kV charge (open circuit )
  ≈65 Ω output impedance
  100 ns FWHM
  157 J

## Slide 9: Experimental Results
Result settings
  Backwall : 0mm – 17.5mm in 2.5mm steps
  Bottom plate : 0mm – 32mm in 2mm steps
  AK sweep : 5mm – 24.5mm in .5mm steps
Notes: Quickly skim through this

## Slide 10: E-Field Vs. Frequency @ 3m
Notes: Red arrows shows old tube frequencies
Blue shows microwave patterns in future slides

## Slide 11: Frequency Vs. AK, E-Field > 25KV
Notes: Shows the frequency steps for different AK settings while showing the different BW settings

## Slide 12: Settings Showing Frequency Movement

## Slide 13: Settings Showing Frequency Movement

## Slide 14: 2GHz Shot Summary
Total estimated radiated power ≈139MW
Estimated efficiency ≈ 13.4%
  Calculated from Marx Energy & pulse width
  RF was considered rotationally symmetric across beam spot

## Slide 15: 5.36GHz Shot Summary
Total estimated radiated power ≈ 77MW
Estimated efficiency ≈ 7.5%
  Calculated from Marx Energy & pulse width
  RF was considered RF was considered rotationally symmetric across beam spot

## Slide 16: 5.36GHz Mode Pattern

## Slide 17: 2GHz Mode Pattern
Notes: Slide is hidden from the audience

## Slide 18: Summary
Achieved wide tuneability of a sealed Vircator tube.
Long life time >
Rep-rate able to 100Hz
Fully automated system
  Microprocessor ran system
    Air valves
    Tuneability via 4 stepper motors
    Charging
    Firing
Future work
  Determine mode competition